This page was exported from TerraBound Solutions Inc. [    https://www.terraboundsolutions.com    ]

Export date: Tue Apr 16 4:30:52 2024 / +0000 GMT

# Sit & Stay Bench

Price: $999.00

SKU: 61-pbark940

Product Page: https://www.terraboundsolutions.com/product/sit-stay-bench/

## Product Summary

Dimensions: 72"L x 35 3/16"H x 23 3/16"W

Seat Height: 16 15/16"

## Product Description

As part of our Dog Park Equipment accessories we're pleased to feature this laser cut dog themed park bench. Detailed to coordinate with your dog park play components. This bench is thermoplastic coated for superior durability and beauty. Choose green or blue planks with black frames to coordinate with your personal aesthetic needs.

- Seats and Back:11 gauge die formed angle frame 1”x1-7/8” with 3” radius corners. Seat and back plates are fabricated from a 12ga plate. Holes are precision punched at 5/8” diameter. 7 gauge x 1-1/2” flat bar center support and mounting bracket understructure. Electrically MIG welded.

- Coating: Oven fused functionalized polyethylene copolymer-based thermoplastic. Fluidized bed coating application with superior mechanical performance, impact resistance and UV-stability.

- Frame:2-3/8” O.D. x 12 gauge pre-galvanized structural steel tubing. Seat/back support is bent over a mandrel through the bend radius producing a wrinkle free bend. Tube ends are pre-galvanized steel capped. Seat mounting points are 7 gauge x 1-1/2” die stamped steel flat bar. Cross braces are 1.029 O.D. x 15 gauge pre-galvanized structural steel tubing. All electrically MIG welded.

- Frame Coating: Electrostatic powder coated application oven cured.

- Dimensions: 6' bench portable with back. Seats and back are 12-1/8” wide x 72-1/8” long. Seat height is 17”, seat back height is 35”. Total depth of seat with back is 22”.

Product export as MS Document by WooCommerce PDF & Print plugin.